## Slide 1: Analog Circuit Set-up

## Slide 2: MQ3 Set-up
FPGA Board
JXADC
A13: Analog Signal
A14: Ground Reference
GND
Launchpad
MQ-3
Potentiometer
5V source

## Slide 3: Caution:
Remember to make sure the voltage sent to the FPGA analog pins need to be in the safety limit of 0-1 V
  Signals beyond this can break these pins
  You can tune the amount of resistance for achieving this range by rotating the potentiometer accordingly.
    Best practice is to used an oscilloscope or multimeter to observe sensor signal range before connecting to FPGA. IR distance or MQ3 sensors are good for finding the best range.
Be sure that all pieces share a common ground. For this demonstration, Launchpad Ground is this common ground.